## Slide 1: History of Construction Code in Korea
Kwon, O-Cheol
Daelim University College / Architecture Engineering Department

## Slide 2
Introduction
1950s (1950~1960)
1960s (1961~1970)
1970s (1971~1980)
1980s (1981~1980)
1990s (1991~2000)
2000s (2001~ )
Conclusion
Index

## Slide 3
Construction Standards
  According to Article 44 of the Construction Technology Promotion Act
  Criteria for the technical and environmental improvement, quality assurance and appropriate construction management
  Central construction technology deliberation target: There are specifications (standard specifications, specialized specifications) and design standards.
  Sub-technical standards prepared by societies, associations, and ordering organizations: guidelines, handbooks, technical guides, tips, standards, etc.
Introduction
 |  | Law (Enforcement Decree, Enforcement Rule) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
instructions |  |  | established rule |  |  | precept |  |  | notice |  |  |  |  | Announcement |  | 
Design criteria |  | Ministry of Land, Infrastructure and Transport, etc. Management |  |  |  | Standard Specification |  | Ministry of Land, Infrastructure and Transport, etc. Management |  |  |  |  |  | Professional Specifications |  | Ministry of Land, Infrastructure and Transport, etc. Ordering Agency
Sub-technical standards (guidelines, handbooks, technical guides, tips, standards) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Ministry of Land, Infrastructure and Transport

## Slide 4
Definitions and Sources of Terms Related to Construction Standards
Introduction
Terms | Definition of Terms | source
Construction standards | Criteria for the improvement of technical and environmental characteristics of construction work, quality assurance, and proper construction management | Construction Technology Promotion Act Article 44
Design Standards | Criteria that stipulates the limits (minimum limits) of design conditions for the designer to maintain quality, strength, safety, performance, etc. for facilities or work in carrying out design work for each facility | Preparation and management of design standards for construction works
Standard Specification | Standard construction standards set for each facility to ensure safety of facilities and appropriateness and quality of construction execution | Article 65 Paragraph 6 of the Enforcement Decree
Professional Specifications | Comprehensive construction standards for use in the construction of specific construction projects or the preparation of construction specifications for all types of construction based on the standard specifications for each facility | Article 65 Paragraph 7 of the Enforcement Decree
Sub-technical Standards | Standard drawings, guidelines, handbooks, technical guides, work instructions, etc. that define the contents of design and construction standards in more detail | Article 40 of the Operational Regulations on Construction Technology Development and Management

## Slide 5
1950~1953: Korean War
  A view of the city of Seoul in ruins after the war
Introduction
http://www.100ssd.co.kr/news/articleView.html?idxno=17435
http://www.100ssd.co.kr/news/articleView.html?idxno=17435
http://www.wolyo.co.kr/news/articleView.html?idxno=32624

## Slide 6
Current view of downtown Seoul
Introduction
https://blog.naver.com/skkim3378/221545258169
https://www.doopedia.co.kr/photobox/comm/community.do?_method=view&GAL_IDX=200615001235986#hedaer

## Slide 7
History of Construction Standards
  Investigate the history of changes in construction standards in 10-year units from the 1950s to the present.
  Construction standards were enacted and revised while reflecting the economic and social issues, events, accidents, and problems of the time.
  Investigate social and economic trends by year. completed construction facilities
  Find out about incidents, accidents, and representative by year.
  Comprehensively examining changes in construction-related standards in Korea.
Introduction

## Slide 8
Changes in national income from 1950 to the present
  1950-1953: Post-war recovery period after the Korean War (US$ 100 or less)
  GNI per capita in 1963: US$103
  GNI per capita in 1977: US$ 1,053 (after 14 years)
  GNI per capita in 1994: US$ 10,357 (after 17 years)
  GNI per capita in 2006: US$ 21,664 (after 12 years)
  GNI per capita in 2017: US$ 31,734 (after 11 years)
Introduction
1994
US$10,357
2006
US$21,664
2017
US$31,734
1977
US$1,053
1963
US$104
통계청 https://kosis.kr/statHtml/statHtml.do?orgId=301&tblId=DT_111Y002&checkFlag=N

## Slide 9
  Recovery period after war
  1950.12~ : The United Nations Korea Reconstruction Agency(UNKRA) aids in Korean reconstruction
  1953~ : Restoration and renovation of SCO facilities with assistance from the US Foreign Operation Administration (FOA)
  Restoration of roads, railways, and power generation facilities damaged by war, and promotion of construction work such as thermal power and hydroelectric power plants
  Severe housing shortage due to mass destruction of houses due to war
    1951~1956: Construction of 197,000 emergency relief houses
    1951~1962: A total of 910,000 housing units were built nationwide.
    1958. 7.18: Announcement of the first apartment sale in Korea
  1952: Completion of Goesan Dam
  1956. 5: Completion of Dangin-ri Thermal Power Plant
1950s (1950~1960)

## Slide 10
Recovery period after war
  View of a shack in downtown Seoul • Korea's first apartment for sale (In 1958)
  Goesan Dam (In 1952) • Danginri Thermal Power Plant Units 1, 2, 3 (In 1956)
1950s (1950~1960)

## Slide 11
  Period of foundation for post-war reconstruction and building projects according to industrialization and modernization
  When resource and industrial complex development began
  1st Economic Development Plan(1962~1966): Expansion of key industries and social overhead capital
  2nd Economic Development Plan(1967~1971): A leap forward for the construction industry for 10years
    Rapid growth and structural change of the Korean economy: increased exports, unprecedented boom in the construction industry
  GNI per capita in 1963: US$103
  Housing sector
    Intensifying the problem of lack of quantity and poor quality
    Construction of 866,200 units in 10 years
1960s (1961~1970)

## Slide 12
Facilities and construction standards completed in the 1960s
  1962: National Construction Research Institute established
  1962. 12: Completed Jangchung Gymnasium
  Chuncheon dam construction in 1965, Seomjingang multi-purpose dam construction in 1965, Uiam dam construction in 1967, Namgang multi-purpose dam construction in 1969
  1969: Completion of 29.5 km of Gyeongin Expressway (Secure the 7th expressway in the world)
  1968. 2.1 ~ 1970. 7. 7: Completion of 428 km of Gyeongbu Expressway
  1970. 10: Samil Building (2 stories below, 31 above the ground), the tallest building in Korea at the time
  As government-ordered projects become larger and more technologically advanced, construction technology inevitably improves rapidly
  Railroad Act (1961), Road Act (1961), River Act (1961), Water Supply Act (1961), Survey Act (1961) enacted
  Urban Planning Act (1962), Building Act (1962), Medium-term Management Act (1966), Port Act (1967) enacted
  Revisions to the building law in the 1960s
    Contents related to disasters in buildings in connection with the Urban Planning Act
    Unlicensed housing, industrialization and security issues centered on large cities: Designation of maximum and minimum heights for permitted architectural uses by area of use
    Fire regulations focusing on safety and fire extinguishing
    Introduction of regulations such as underground floor installation, parking lot installation reinforcement, standard design drawings, heat loss prevention, etc.
1960s (1961~1970)

## Slide 13
  Samil Building (In 1970) • Jangchung Gymnasium (In 1962)
  Opened Gyeongin Expressway (In 1969)
1960s (1961~1970)

## Slide 14
  Aim for US$10 billion in exports and US$1,000 in GNP per capita
  First Comprehensive National Land Development Plan (1972~1981)
    Efficient use of land for efficient economic growth
    Establishment of the foundation for national land development to support economic growth
    Environment conservation according to the development of land-owned resources and the development of large-scale industrial complexes
    Improvement of urban problems and improvement of living environment
  Excessive concentration of urban population, deepening polarization of the land, and environmental destruction caused by development are on the rise.
  Achieved US$1,053 per capita gross national income in 1977
  Urbanization rate of 66.4% and housing supply rate of 71.2%
1970s (1971~1980)

## Slide 15
  In 1972, International commodity price surge
  In 1973, The first oil shock
  The scale of the economy in the 1970s shifted from a developing country to an industrial-oriented developing country.
  1967. 4~1973. 10: Completion of Soyanggang Multi-purpose Dam (Storage capacity of 2.9 billion tons)
  1974. 8. 15.: Seoul Subway Line 1 opened (total 98.6km)
  1970. 9~1978. 4.: Completed Kori Nuclear Power Plant No. 1 (21st in the world, 3rd in Asia)
  Seoul Subway Line 1 opened (In 1974) • Completion of Soyanggang Dam (In 1973)
    ← Kori Nuclear Power Plant Unit 1 (In 1978)
https://namu.wiki/w/%EC%86%8C%EC%96%91%EA%B0%95%EB%8C%90
1970s (1971~1980)

## Slide 16
Date of occurrence | April 8, 1970
Causes | Poor construction
Harm | complete collapse of the building 34 dead, 40 injured
Measures | Implementation of prevention of poor construction
https://w.namu.la/s/cb0d66188c78ff015b5a314f9e4e86fddf441d4583e50a450fd022ab9e676d4b5dfc0055b5c96df0ad6c73837c08230fab406e2e4ec704cc786b3c0305c162d88f6dab33115458cc8a3de07df2fa0c60b2aa719eb44e083eb3064d0085a8dee3907a484417ef180ddb31cb69c36dfbc3
Wow Citizen's Apartment Collapse (In 1970)
https://ko.wikipedia.org/wiki/%EC%99%80%EC%9A%B0%EC%95%84%ED%8C%8C%ED%8A%B8_%EB%B6%95%EA%B4%B4_%EC%B0%B8%EC%82%AC
https://upload.wikimedia.org/wikipedia/commons/thumb/f/f8/1970%EB%85%84_4%EC%9B%94_8%EC%9D%BC_%EC%84%9C%EC%9A%B8%ED%8A%B9%EB%B3%84%EC%8B%9C_%EC%99%80%EC%9A%B0%EC%95%84%ED%8C%8C%ED%8A%B8_%EB%B6%95%EA%B4%B4_%EC%B0%B8%EC%82%AC2.jpg/1280px-1970%EB%85%84_4%EC%9B%94_8%EC%9D%BC_%EC%84%9C%EC%9A%B8%ED%8A%B9%EB%B3%84%EC%8B%9C_%EC%99%80%EC%9A%B0%EC%95%84%ED%8C%8C%ED%8A%B8_%EB%B6%95%EA%B4%B4_%EC%B0%B8%EC%82%AC2.jpg
1970s (1971~1980)

## Slide 17
Daeyeongak Hotel Fire Accident (In 1971)
Date of occurrence | December 25, 1971
Causes | LP gas explosion
Harm | building burnout 191 dead, 63 injured
Measures | Establishment of regulations related to evacuation and fire prevention in high-rise buildings
https://m.blog.naver.com/PostView.naver?isHttpsRedirect=true&blogId=nunuari&logNo=220597864914&view=img_2
https://historylibrary.net/entry/%EC%88%9C%EA%B0%84%ED%8F%AC%EC%B0%A9-%ED%81%AC%EB%A6%AC%EC%8A%A4%EB%A7%88%EC%8A%A4-%EC%95%85%EB%AA%BD-%EB%8C%80%EC%97%B0%EA%B0%81%ED%98%B8%ED%85%94-%ED%99%94%EC%9E%AC-%EB%8C%80%EC%B0%B8%EC%82%AC
1970s (1971~1980)

## Slide 18
  10-year housing construction plan(1972~1981)
    Target to build 2.5 million homes nationwide
    In 1972, the Housing Construction Promotion Act was enacted.
  In 1975, Overseas Construction Promotion Act enacted. Support for construction companies to enter the Middle East construction market
  Building Code Revision History
    Most government-led regulations are newly established and strengthened, and preventive supervisory regulations have been introduced and strengthened.
    In particular, security and factory-related environmental pollution prevention regulations, urban overcrowding prevention, urban aesthetics, efficient use of land, housing shortage, fire related regulations and penalties, parking lots, energy conservation, simplification of civil complaints and strengthening of regulations.
    Firefighting related regulations, energy saving, and security regulations are newly established due to domestic and foreign incidents such as large fires and oil shocks.
    New regulations regarding environmental pollution prevention regulations, pollution prevention and standard design drawings of factories.
    Preparing rules for prevention through the establishment of construction supervision, interim inspection, and maintenance systems.
    In the 1960s, fire regulations focused on safety and fire extinguishing, and in the 1970s, regulations for early ignition prevention, evacuation from high-rise buildings, and buildings that are prone to fire were newly established.
1970s (1971~1980)

## Slide 19
  The period when national infrastructure began to be reorganized and full-scale urbanization took place
  National and regional plans are pouring in, and construction of 2 million houses is promoted
  Distribution of growth emerges as a major issue
  Promotion of the 2nd comprehensive national land development plan
  In order to correct the phenomenon of overcrowding in the metropolitan area centered on Seoul, the Seoul Metropolitan Area Reorganization Plan is implemented and development profit recovery measures are implemented
  With the complete revision of the Urban Planning Act, the foundation for new town development was established by establishing a basic urban plan, institutionalizing resident participation, and enacting the Housing Site Development Promotion Act (Bundang, Ilsan, etc.)
1980s (1981~1990)

## Slide 20
Construction Environment
  Changes in the construction industry environment
    Rapid decrease in construction orders: The scale of overseas construction orders also decreased sharply in the aftermath of the second oil shock
    Fierce competition for orders due to reduction in construction volume
    In 1989, Manpower shortage and material shortage due to the construction of 2 million housing units
  1981. 10: Establishment of Han River Comprehensive Development Project
  1980.2~1985.5: Completion of Building 63 (the tallest building at the time, 3 stories below and 60 above the ground)
  1986 Independence Hall fire incident
    Improvement of the construction system and measures against poor construction: fundamental prevention of poor construction work
    Since then, construction companies have established a technology research institute and expanded investment in technology development.
  Hosted the 1986 Asian Games and the 1988 Seoul Olympics
  In 1988. 5: Establishment of the 2 million housing construction promotion plan (1988~1992)
    Development of 5 large-scale new towns in the metropolitan area
1980s (1981~1990)

## Slide 21
  Han River Comprehensive Development Project (In 1981)
  88 Seoul Olympic Stadium
1980s (1981~1990)

## Slide 22
  63Building (1985)
    63 Fl : B3F / 60 F, 274m
1980s (1981~1990)
https://w.namu.la/s/66fb39dc1a2dff842136423cdfc056fd9b04e33d264d31d2ef48b1879f01d703385fcf51842727dc5db65cee1ec847491cee52ded76700798b732ffd4b90c347faa833f4a533ad5c8b55e2a02d3cba6d6d2eab4a9479d20076f20b2bf2ecba44fb601c663ceade5f093cd2299ffbac66

## Slide 23
Independence Hall Fire Accident (1986)
Date of occurrence | August 4, 1986
Causes | Electrical short circuit due to poor construction
Harm | main building roof burnout
Measures | Improvement of construction system and measures to prevent insolvency (1987. 2) Improvement of the license system Improvement of the bidding and contract system Establishment of responsible construction and supervision system Soundness of the subcontracting relationship Construction Technology Management Act enacted
https://m.blog.naver.com/PostView.naver?isHttpsRedirect=true&blogId=dper2000&logNo=70091659319
1980s (1981~1990)

## Slide 24
  Building Code Amendments
    Reinforcement of preventive regulations to prevent poor construction in advance based on the mitigation direction
    Regulations are prepared to reflect the introduction and activation of multi-family housing, the introduction of urban design, and the relaxation of the floor area ratio
    Housing shortage regulations, simplification of civil complaints, regulations on deregulation, urban aesthetics, urban overcrowding, penalties, security, ordinance regulations, disabled people and earthquake regulations are highlighted
    Introduction of the urban design system and resident supervision system, and expansion of the object of construction report
  Enactment of Construction Technology Management Act (October 24, 1987)
    Enactment of Construction Technology Management Act to promote technology development in the construction industry in the wake of the fire at Independence Hall
    Unification of the ‘Construction Industry Act’, ‘Technical Service Promotion Act’, and ‘National Technical Qualification Act’ scattered across government ministries
    At that time, when the construction industry entered overseas markets, it was judged that it was urgent to develop construction technology in preparation for the increase in orders for technology-intensive construction and the upcoming domestic construction market opening.
1980s (1981~1990)

## Slide 25
  3rd comprehensive national land development plan stage : social interest in quality of life and environmental issues
  urbanization rate 88.3%, housing supply rate 96.2%
  Seongsu Bridge and Sampoong Department Store collapse, IMF bailout, etc. Social and economic difficult times
  In accordance with the government's globalization and localization policy, we aim to prepare domestic building standards that meet international standards, simplify civil complaints, and eliminate regulations
  In line with the succession of major building disasters, the law on building safety standards and inspections has been strengthened
  Significantly simplify the construction procedure, supplement the construction supervision system to improve the quality of buildings, and strengthen penalties for poor design and construction supervision
  Achieved per capita gross national income of US$10,357 in 1994 (17 years required)
1990s (1991~2000)

## Slide 26
  Large-scale accidents : the collapse of the Olympic Bridge, the collapse of the Paldang Bridge, the collapse of the Sinhaengju Bridge, the collapse of the Cheongju Uam Shopping Mall, the collapse of the Seongsu Bridge, the explosion of the Daegu subway construction site, and the collapse of the Sampoong Department Store
  1993. 12: Market opening of all industries according to the Uruguay Round (UR) agreement
  1993. 8. 12: Implementation of real-name financial system
  1995. 7: Real-name real estate system
  1995: World Trade Organization (WTO) launched
  1996: The era of full-scale liberalization of the construction market by joining the Organization for Economic Cooperation and Development (OECD)
  1996. 12: Enactment of the Framework Act on Construction Industry- Extensive overhaul of construction systems and policies for the opening of the domestic construction market in accordance with globalization and major construction-related accidents
  1997.12: International Monetary Fund (IMF) foreign exchange crisis: restructuring of the construction industry
  Summary of the construction industry environment in the 1990s: bubble, insolvency, openness, restructuring
1990s (1991~2000)

## Slide 27
1998 : Malaysia Petronas Twin Tower
  1998 ~2003 : World Tallest Building, 88 Floor, 452m
1990s (1991~2000)

## Slide 28
Sinhaengju Bridge pier collapse (In 1992)
Date of occurrence | July 31, 1992
Causes | Poor construction
Harm | bridge collapse 34 dead,40 injured
Measures | Establishment of measures to prevent insolvency in construction work Introduction of Responsibility Management System to Public Corporations Introduction of the pre-bidding qualification screening system
https://upload.wikimedia.org/wikipedia/commons/thumb/e/ed/1992%EB%85%84_7%EC%9B%94_31%EC%9D%BC_%EC%8B%A0%ED%96%89%EC%A3%BC%EB%8C%80%EA%B5%90_%EB%B6%95%EA%B4%B4%EC%82%AC%EA%B1%B4.jpg/2560px-1992%EB%85%84_7%EC%9B%94_31%EC%9D%BC_%EC%8B%A0%ED%96%89%EC%A3%BC%EB%8C%80%EA%B5%90_%EB%B6%95%EA%B4%B4%EC%82%AC%EA%B1%B4.jpg
https://news.kbs.co.kr/data/news/2015/07/31/3122438_4ZB.jpg
1990s (1991~2000)

## Slide 29
Collapse of Cheongju Uam Shopping Street Apartment (In 1993)
Date of occurrence | January 7, 1993
Causes | Poor construction (rebar spacing, insufficient thickness of fireproof coating, etc.) Gas explosion
Harm | Collapse of buildings 28 dead, 48 injured
Measures | Identification of construction irregularities and measures to prevent those Establishment of the Anti-Corruption Countermeasures Committee under the leadership of the Board of Audit and Inspection
https://namu.wiki/jump/hddQj3rLt0QUnDB5STmlDI%2FIZiESCV%2Bm%2FCI0TlZ3aRkqgJOrolOYKiZpb0qV6Lsk
1990s (1991~2000)

## Slide 30
Seongsu Bridge Collapse Accident (In 1994)
Date of occurrence | October 21, 1994
Causes | Poor construction: Poor welding of truss connection joints Neglect of maintenance and inspection
Harm | 32 dead, 17 Injured
Measures | Enactment of Special Act on Facility Safety Management Permission to enter foreign supervisory companies, introduction of design supervision system, establishment of comprehensive supervision system improvement plan Strengthening the safety management system of existing facilities
https://upload.wikimedia.org/wikipedia/commons/thumb/6/6f/2000%EB%85%84%EB%8C%80_%EC%B4%88%EB%B0%98_%EC%84%9C%EC%9A%B8%EC%86%8C%EB%B0%A9_%EC%86%8C%EB%B0%A9%EA%B3%B5%EB%AC%B4%EC%9B%90%28%EC%86%8C%EB%B0%A9%EA%B4%80%29_%ED%99%9C%EB%8F%99_%EC%82%AC%EC%A7%84_1994%EB%85%84_%EC%84%B1%EC%88%98%EB%8C%80%EA%B5%90%EB%B6%95%EA%B4%B4.JPG/1280px-2000%EB%85%84%EB%8C%80_%EC%B4%88%EB%B0%98_%EC%84%9C%EC%9A%B8%EC%86%8C%EB%B0%A9_%EC%86%8C%EB%B0%A9%EA%B3%B5%EB%AC%B4%EC%9B%90%28%EC%86%8C%EB%B0%A9%EA%B4%80%29_%ED%99%9C%EB%8F%99_%EC%82%AC%EC%A7%84_1994%EB%85%84_%EC%84%B1%EC%88%98%EB%8C%80%EA%B5%90%EB%B6%95%EA%B4%B4.JPG
https://lh3.googleusercontent.com/-Kn3bJEAi8U0/W0yJmA48rCI/AAAAAAADIS8/OIeQ3ytPjeQ9EFhq6Z9o-lh0f6W086pXgCHMYCw/s0/8deefa897b5356202f69fb6bbbfc4bf63e9a409f.jpg
1990s (1991~2000)

## Slide 31
Daegu Subway Gas Explosion Accident(1995)
Date of occurrence | April 28, 1995
Causes | City gas pipe penetration during subway construction excavation Gas leak explosion
Harm | 101 dead, 202 injured
Measures | Preparation of measures to strengthen the safety management system for underground excavation sites Computerization of information related to underground facilities and reinforcement of management of underground excavation sites, etc.
https://w.namu.la/s/77212ba03bf243556308218899622445c017d96a18e1af17cc67a495801b96c350ca7856674c3b3b753b02df2c2ccaa133e36897709a7a3d9843d034e915d228d5f21a454245d99132b1336c6fafd4ee
1990s (1991~2000)

## Slide 32
Sampung Department Store Collapse Accident (1995)
Date of occurrence | June 29, 1995
Causes | Poor construction Illegal unauthorized extension and structural change (free plate structure)
Harm | Partial complete collapse of a building 502 dead, 937 injured, 6 missing
Measures | Reinforcement of design and supervision of private multi-use buildings, etc. Establishment of measures to prevent poor construction and secure building safety
https://img8.yna.co.kr/photo/old/data2/orign_img/2002/08/19/2020819_0021_P4.jpg
https://blog.kakaocdn.net/dn/b5I92s/btq6RIHaJ7H/tICEUi2ajWbKB3TXfo0sOK/img.jpg
1990s (1991~2000)

## Slide 33
Enactment of Special Act on Facility Safety Management (1995. 1. 5)
  Legislation was enacted as a system to ensure the safety of maintenance and management of facilities after completion in response to continuous safety accidents such as the collapse of Seongsu Bridge and the collapse of Sampoong Department Store
  Periodic safety inspection institutionalization of 30,000 major facilities nationwide (bridges, tunnels, dams, subways, multi-use buildings)
  Mandatory safety measures such as repair and reinforcement according to inspection results
  Establishment of a facility information system that computerizes the life cycle history of facility design, construction, diagnosis, and incidents
Establishment construction information system
  After the Daegu subway gas explosion, the need for construction information for the safety management of facilities emerged
  Establishment of ‘Construction Information Integrated Computer Network’ to prevent poor construction
    Integrated management of information generated in the entire process of planning, design, contract, construction and maintenance of construction work
  Standardize design, materials and construction methods
At January 13 1997, Revision of Construction Technology Management Act
: Mandatory establishment of safety management plan
1990s (1991~2000)

## Slide 34
2000’s
  It is the 4th comprehensive national land development plan stage, and the plan that started in the 1960s has ended.
  As the time to emerge as a central country in Northeast Asia, advanced country-type land management plans began to be pursued, and balanced regional development and sustainable land management were emphasized.
  Urbanization rate 85.4% in 2015
  In 2002, the housing supply rate exceeded 100%
  Achieved US$21,664 in GNI per capita in 2006
2000s (2001~ )

## Slide 35
2001. 3 : Incheon International Airport opend
  Phase 1 (2001) Phase 2 (2008)
  Phase 3 (2017) Phase 4 (2024)
2000s (2001~ )
https://www.airport.kr/ai/ko/index.do

## Slide 36
2001. 11 : Opend Seoul World Cup Stadium
2000s (2001~ )
https://ww.namu.la/s/9ff4f722de0faf71743a4df184c17f894dd84c98a273d59b2ea88ef02b6acbda16cd25ca5221fd91849b53fb2b1548a37598e9e212a8fbbc820681f2e6f9e61caa36464733aac20636de7d7ac5aa756461623d557ba85e6d8ac380475f8f33cf59d5f68128fc08f57ebfdc6a5ec1dfd2
https://ww.namu.la/s/9ff4f722de0faf71743a4df184c17f894dd84c98a273d59b2ea88ef02b6acbda16cd25ca5221fd91849b53fb2b1548a37598e9e212a8fbbc820681f2e6f9e61caa36464733aac20636de7d7ac5aa756461623d557ba85e6d8ac380475f8f33cf59d5f68128fc08f57ebfdc6a5ec1dfd2

## Slide 37
2003 : Taiwan Taipei 101 Tower
  101 Floor, 509m
  2003 ~ 2010 World Tallest Building
2000s (2001~ )
https://en.wikipedia.org/wiki/Taipei_101#/media/File:Taipeh_Taipei_101_16.jpg

## Slide 38
2004. 4. 1 : Gyeongbu high-speed railway line
  5th Country with high-speed rail in the World
  Seoul-Pusan 417km : 2H 18Min
  Max Speed : 305 km/h
2000s (2001~ )
http://www.mcnews.co.kr/imgdata/mcnews_kr/201012/20101203_094518_559f369.jpg
http://www.mcnews.co.kr/imgdata/mcnews_kr/201012/20101203_094518_559f369.jpg

## Slide 39
2009 10 : Incheon Bridge
  21.38 km Length
  1st Longest Bridge in Korea
2000s (2001~ )
https://ww.namu.la/s/54cd7f5bf772e24b18ef76c5ba95bfa6edfea4da51faa09b1d1e20329dcec912c0783924051e98588050ee792ef1420cede85fd282c2aa8b95c0ddf37b8b187bd9a3bd7d3c5ea39370cc407d34b2b9d9d59d4173acaf323940d9fbb5d0495441a506eda086f66c92fe7a72d0080c30c4
https://w.namu.la/s/c1d3c3a4a7f2de95c141ce9d0dc794e67f46be0b4f745a5d135ce6cb38e3f15bc74fcd0f6a0efd50172a2daa1b117679a6d1b035ee3c7a5946ee6f3d29cd6c6071a9460dd9dde52c0b5c69114dddc17989ad8e65621131ffd1d04a3487984440

## Slide 40
2010 : Dubai Burj Khalifa
  163 Floor, 829m
  2010 ~ Current : the tallest building in the world
2000s (2001~ )

## Slide 41
2017. 2 : Lotte World Tower
  B6 / 123 FL, 555m
  Currently the tallest building in Korea
2000s (2001~ )
https://dimg.donga.com/egc/CDB/SHINDONGA/Article/14/90/86/14/1490861426859.jpg
https://www.hankyung.com/economy/article/2020072092451

## Slide 42
Fire in Icheon Refrigerated Warehouse
Date of occurrence | January 7, 2008
Causes | Misfire caused by welding sparks
Harm | Total burnout of the building 40 dead, 9 injured
Measures | 
https://t1.daumcdn.net/cfile/blog/165D4C594DF7931C2B
http://www.fpn119.co.kr/imgdata/fpn119_co_kr/200812/200812235505875.jpg
2000s (2001- )

## Slide 43
  In 2014, Gyeongju Mauna Resort Gym Collapse Accident
Date of occurrence | February 17, 2014
Causes | Use of PEB method to finish with sandwich panel on the steel structure of the gym Heavy snow: The snow load standard itself was low, and the snow removal work was insufficient.
Harm | Building collapse 10 dead, 124 injured
Measures | 
https://news.sbs.co.kr/news/endPage.do?news_id=N1002264872
2000s (2001~ )

## Slide 44
Sewol ferry sinking
Date of occurrence | April 16, 2014
Causes | Lack of stability due to vessel extension, overload, rapid change of route, etc.
Harm | Ferry sinking 299 dead, 5 missing
Measures | A reminder to strengthen the safety system for society in general in Korea
https://namu.wiki/w/%EC%84%B8%EC%9B%94%ED%98%B8
https://www.donga.com/news/Society/article/all/20200117/99266838/1
2000s (2001~ )

## Slide 45
  Earthquake
Location | Gyeongju | Pohang
Date of occurrence | September 12, 2016 | November 15, 2017
Causes | Richter 5.8 magnitude earthquake | Richter 5.4 magnitude earthquake
Harm | 23 injured, property damage 11 billion won | 135 injured, Property damage 332.3 billion won
Measures | Expansion of buildings subject to seismic design duty | 
https://blog.naver.com/ijtj7872/221156969217
2000s (2001~ )
https://img0.yna.co.kr/photo/yna/YH/2016/09/13/PYH2016091300680005200_P4.jpg

## Slide 46
Nationwide sinkhole (ground subsidence) occurrence
https://www.hankookilbo.com/News/Read/202002141818723340
https://newsis.com/view/?id=NISX20210901_0001567739
https://www.hankyung.com/society/article/2020082693117
https://www.joongang.co.kr/article/22944761#home
2000s (2001~ )

## Slide 47
  1999. 3: Introduction of the CM(construction management
  2001. 12: Systematized management of design documents to strengthen facility safety management
  2008. 1: Prevention of poor feasibility of large-scale national projects
  2008. 8: Reinforcement of the responsibility of construction participants for insolvency and safety accidents due to the increase in safety accidents and accidents at construction sites
  2008: Building Framework Act enacted: Acting as the parent law in the field of architecture. Present the goals, directions, outlines, etc. of national policies and systems in the field of architectural administration
  2009. 12: Reinforcement of career management for construction engineers to prevent insolvency and improve quality of construction work
  2010. 1: Reinforcement of ex post evaluation of public works by revision of implementation guidelines for ex post evaluation of construction works
  2014: Prevention of noise between households and floors, prevention of crime in buildings, reinforcement of material safety in indoor construction
  2015 : Prevention of Safety Accidents in Special Structured Buildings Following the Gyeongju Mauna Resort Collapse Accident
2000s (2001~ )

## Slide 48
  2014. 4: Establishment of the National Construction Standards Center (reorganization of complex construction standards)
  2015. 7: Structural review of temporary structures and confirmation of structural safety of temporary structures during construction
  Following the Sewol ferry sinking accident in 2015, the National Ministry of National Safety was established and the construction safety management system was strengthened
  2015: Reinforcement of ground investigation due to occurrence of sinkholes (ground subsidence) nationwid
Construction Technology Promotion Act enacted (2014. 5)
  Enforcement of the full revision of the Construction Technology Management Act to the Construction Technology Promotion Act
  Reinforcement of support for construction technology and construction services by shifting from ‘management’ to ‘promotion’
  The purpose of securing competitiveness of construction technology services in the global construction market
  Improvement of the construction technical manpower management system, fostering of construction technology service industry, integration of supervision and CM, etc.
  Index of Construction Engineer’s Competency, ICEC: Comprehensive evaluation of technician experience, academic background, and qualifications
2000s (2001~)

## Slide 49
Building Code Amendments
Year | Contents
2005 | Creating a comfortable living environment: Added a part related to indoor air quality to the building finishing material standards
2006 | Introduction of eco-friendly building certification system
2006 | house performance rating system
2008 | Implementation of the Green New Deal policy to overcome the global financial crisis and expand finance: support for low-carbon green growth
2008 | Establishment of building energy efficiency rating certification system
2010 | Clarify noise and vibration management targets. Create a noise map. Construction site noise measurement
2011 | Induce the activation of intelligent building construction by introducing the intelligent building certification system
2012 | High-rise building definition: A building with 30 stories or more than 120m in height. Check whether seismic performance is secured
2012 | Enactment of Green Building Support Act
2000s (2001~)

## Slide 50
After the Korean War in 1953, GDP per capita grew rapidly from US$103 per capita in 1963 to US$31,734 in 2017
  The contribution of the construction industry to Korea's economic development is very high
  There are many symbolic and landmark facilities in Korean construction history
  Construction standards are continuously enacted and revised according to economic, social, and political conditions by year
  Many parts have been remarkably improved with preventive measures caused by various construction accidents
  In particular, after a major construction accident in the 1990s, the construction standards underwent many changes
  Currently, it possesses world-class construction technology in skyscrapers, bridges, and tunnels
  Continuous revision work is necessary in the future social and economic flow
Conclusion