## Slide 1: Localization of passive house construction
Oh, Dae-seok
Passive House Institute Korea

## Slide 2
Carbon neutral & Zero energy building
  Korea declaration of net zero in 2050
  Energy Zero Building
Localization
  Climate
  South Window
  Shading
  Envelope U-value
  Thermal Storage
  Lifestyle
Zero Energy Building - EDC
Introduction

## Slide 3
2050
carbon neutral
2019.09 EU declaration of net zero in 2050
2020.09.22 Declaration of carbon neutrality in China in 2060
2020.10.26 Japan declared net zero in 2050
2020.10.28 Korea declaration of carbon neutrality in 2050

## Slide 4
Korea declaration of net zero in 2050
01
02
03
04
The damage caused by climate change is estimated to increase to 20% of global GDP annually
Global problem
Country - Energy Policy
40% reduction compared to 2018, the peak emission level (4.17%/year reduction) 2050 Net zero
Industry Development
Develop new market in the field of construction and foster new and renewable energy industry
Developing overseas market by improving international competitiveness
Personal - Reduce energy costs / Ensure a comfortable living environment
Responding to rising energy costs
It is possible to secure a healthy and pleasant living environment
Push!! Push!!
ZEB Responsibility & Want

## Slide 5
Korea declaration of net zero in 2050
  Greenhouse gas reduction roadmap -2021
Korea declaration of net zero in 2050
⇒ (NDC raised level) 40% reduction compared to 2018, the peak emission level (4.17%/year reduction)
Greenhouse gas emissions (million tons CO2)
(NDC upgrade plan)
(NDC current plan)
(Linear reduction by vertex)
(Emission Statistics ‘00~’18)
Source: 2030 National Greenhouse Gas Reduction Target (NDC) Upgrade Plan – 2021-10-18 / Jointly distributed data with related ministries
Notes: 정부의 제로에너지 건축 인증 범위 확대 및 에너지 성능기준 강화 배경
온실가스 감축 로드랩 수정으로 건물 부분의 감축률 상향
- 신축건축물 에너지 기준 강화 - 기존 건축물 그린리모델링 활성화

## Slide 6
Korea declaration of net zero in 2050
  Greenhouse gas reduction roadmap (Architecture part)
Korea declaration of net zero in 2050
- Improve energy efficiency
Expansion of zero-energy building that minimizes energy consumption and green remodeling that improves energy efficiency of old buildings
- Supply of high-efficiency equipment, demand management
Promoting the distribution of high-efficiency devices such as lighting and home appliances, strengthening energy efficiency standards, and strengthening energy demand management
- Smart Energy Management
Installation of sensors and measuring equipment in air conditioning/heating ventilation, lighting, hot water supply, etc., and introduction of real-time automatic energy control system in connection with communication network
- Expanding the supply of clean energy
Expand the supply of new and renewable energy such as solar, geothermal, and water heat, improve the efficiency of district heating heat supply, electrify equipment using fossil fuels, etc.
Source: 2030 National Greenhouse Gas Reduction Target (NDC) Upgrade Plan – 2021-10-18 / Jointly distributed data with related ministries
Notes: 정부의 제로에너지 건축 인증 범위 확대 및 에너지 성능기준 강화 배경
온실가스 감축 로드랩 수정으로 건물 부분의 감축률 상향
- 신축건축물 에너지 기준 강화 - 기존 건축물 그린리모델링 활성화

## Slide 7
Zero energy building
?

## Slide 8
Government's zero energy building certification system
Zero energy building mandatory roadmap
- Establishment of basic green building plan
Announcement of ZEB
- Activation plan
Nowon rental housing pilot project
- Notice of introduction of zero certification system
- Designation of pilot projects by type
- Implementation of zero certification system
- Pilot project completed
- Mandatory for public buildings
more than 1000 square meters
- Technology DB by type
- Mandatory for public buildings
500 square meters or more
- Mandatory for private buildings
(more than 1000 square meters, 30 or more apartment houses)
- Private technology support

## Slide 9
Preparation of legal basis
  Changes in legal insulation performance according to the roadmap
Government's zero energy building certification system
Announcement
of ZEB

## Slide 10
Preparation of legal basis
  Changes in legal window and door U-value according to the roadmap
Government's zero energy building certification system
Announcement
of ZEB

## Slide 11
Government's zero energy building certification system
Zero energy building certification
Zero Energy Building Certification System
- 2020 in public sector
- 2025 in private sector
Minimum requirement
Building energy efficiency 1++ (Residential > 90 kWh/㎡a Non-residential > 140 kWh/ ㎡a)
Energy independency over 20%
BEMS

## Slide 12
Technical point of a zero-energy building
Balance between active and passive
Air tightness
System
window
External awning
Heat exchange ventilation
Active
Passive
Solar power
/ solar hot water system
Geothermal systems
LED
Bio energy
High efficiency
equipment
High insulation

## Slide 13
Technical point of a zero-energy building
Optimum Mixing?
passive
active
Minimum of passive technology
Renewable
energy
High efficiency
equipment
Build Cost
incentive
Client budget
Area, height and tax reduction
Increased Valuation Amount, Low Interest Loans
Optimization
is a combination of factors
that meet the target performance
with minimal cost.

## Slide 14
Technical point of a zero-energy building
Minimum of passive technology
01
02
03
it should satisfy KS A ISO 7730’s thermal comfort such as PMV, PPD, discomfort air flow.
Thermal comfort
Anti-condensation and mold
KS F 2295, Simulation: ISO 15099, KS L ISO 13788 Temperature and humidity performance of building components Critical surface humidity and internal surface temperature calculation to prevent internal condensation
sufficient amount of ventilation
Korea should require the installation of mechanical ventilation for buildings over a certain size and ensure 0.5 ventilation per hour for internal carbon dioxide concentration and pollutant emissions.

## Slide 15
Localization

## Slide 16
Source : Richard Pedranti Architect
- Heat Demand :  15 kWh/(m²a)
- or Peak Heating Load :  10 W/m²
- Primary Energy Consumtion :  120 kWh/(m²a)
- Air Tightness (50pa) :  0.6 /h
Localization of passive house
PHI Passive House standards (Germany)

## Slide 17
Localization of passive house - climate
Climate

## Slide 18
Localization of passive house - climate
Case Study of 1.5L House
  Compare the same building with central Germany and Seoul
  A building with a performance of 1.5 liters in Germany was analyzed with a performance of 1.1 liters in Seoul.

## Slide 19
Climate in Korea and Germany
  Korea is colder in winter and hotter in summer
  High humidity in summer, high discomfort index
More Hot
More Cold
=> More peak load
Seoul (alt.: 20 m, lat.: 37° N)
IBP weather station
Field test site in Holzkirchen
(alt.: 680 m, lat.: 48° N)
More Humidity
=> More mold risk
Localization of passive house - climate

## Slide 20
Climate in Korea and Germany
  2.5 times more winter solar energy than Germany
Localization of passive house - climate
solar gain in winter
Chart: kWh/㎡.month
독일표준 | 30 | 33 | 61 | 101 | 66 | 72 | 82 | 67 | 60 | 28 | 27
서울 | 84 | 87 | 81 | 70 | 59 | 49 | 60 | 75 | 92 | 76 | 80
Seoul
rainy season
Germany
IBP weather station
Seoul (alt.: 20 m, lat.: 37° N)
Field test site in Holzkirchen
(alt.: 680 m, lat.: 48° N)
solar gain in winter

## Slide 21
Traditional Korean Architecture adapted to Regional Climatic Variations
Localization of passive house - climate
Source: http://toytvstory.tistory.com/644

## Slide 22
Region of PHI and Köppen Climate Classification
Localization of passive house - climate
✔
GERMANY = KOREA
WARM TEMPERATE CLIMATE
Source: PHI
5 Types: Climate Classification
Source: Köppen-Geiger vector by Ali Zifan

## Slide 23
Localization of passive house - South Window
South Window

## Slide 24
South solar radiation
  Establishment of strategy to utilize abundant solar energy
Localization of passive house - South Window
solar gain in winter
Chart: kWh/㎡.month
독일표준 | 30 | 33 | 61 | 101 | 66 | 72 | 82 | 67 | 60 | 28 | 27
서울 | 84 | 87 | 81 | 70 | 59 | 49 | 60 | 75 | 92 | 76 | 80
Seoul
rainy season
Germany
IBP weather station
Seoul (alt.: 20 m, lat.: 37° N)
Field test site in Holzkirchen
(alt.: 680 m, lat.: 48° N)
solar gain in winter

## Slide 25
Case study of south window percent
  Comparison of performance by adjusting the area of ​​the south window for 10 certified buildings
Localization of passive house - South Window
case | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | mean
Heat Demand (L) | 2.9 | 3.1 | 3.0 | 2.8 | 2.6 | 2.9 | 3.0 | 2.9 | 2.9 | 3.2 | 2.93
S. Window area | 20.22 | 10.81 | 19.88 | 23.46 | 15.51 | 14.92 | 19.50 | 21.42 | 9.26 | 12.42 | 16.74
S. wall area | 94.28 | 50.85 | 152.72 | 103.88 | 60.65 | 68.11 | 70.61 | 83.87 | 40.69 | 42.96 | 76.86
S. Window % | 21.4% | 21.3% | 13.0% | 22.6% | 25.6% | 21.9% | 27.6% | 25.5.% | 22.8% | 28.9% | 23.1%

## Slide 26
heating demand according to south window percent
  It can be seen that the heating energy performance improves as the area of ​​the south window increases.
Localization of passive house - South Window
S. Window 30%
S. Window 40%
S. Window 50%
S. Window 60%
(L)
(case)

## Slide 27
heating demand according to g-value
  It has the same effect of reducing heat demand with a lower g-value compared to Germany.
Localization of passive house - SHGC (g-value)
Chart: S. Window area (m2)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59
Ug = 0.8, G값 = 0.1 | 4 | 4.1 | 4.1 | 4.2 | 4.2 | 4.3 | 4.3 | 4.4 | 4.4 | 4.5 | 4.6 | 4.6 | 4.7 | 4.7 | 4.8 | 4.8 | 4.9 | 4.9 | 5 | 5 | 5.1 | 5.1 | 5.2 | 5.3 | 5.3 | 5.4 | 5.4 | 5.5 | 5.5 | 5.6 | 5.6 | 5.7 | 5.7 | 5.8 | 5.8 | 5.9 | 5.9 | 6 | 6.1 | 6.1 | 6.2 | 6.2 | 6.3 | 6.3 | 6.4 | 6.4 | 6.5 | 6.5 | 6.6 | 6.6 | 6.7 | 6.7 | 6.8 | 6.9 | 6.9 | 7 | 7 | 7.1 | 7.1 | 7.2
Ug = 0.8, G값 = 0.15 | 4 | 4.1 | 4.1 | 4.1 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.4 | 4.4 | 4.5 | 4.5 | 4.5 | 4.6 | 4.6 | 4.7 | 4.7 | 4.8 | 4.8 | 4.8 | 4.9 | 4.9 | 5 | 5 | 5 | 5.1 | 5.1 | 5.2 | 5.2 | 5.2 | 5.3 | 5.3 | 5.4 | 5.4 | 5.4 | 5.5 | 5.5 | 5.6 | 5.6 | 5.7 | 5.7 | 5.7 | 5.8 | 5.8 | 5.9 | 5.9 | 5.9 | 6 | 6 | 6.1 | 6.1 | 6.1 | 6.2 | 6.2 | 6.3 | 6.3 | 6.3 | 6.4 | 6.4
Ug = 0.8, G값 = 0.2 | 4 | 4 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.3 | 4.3 | 4.3 | 4.4 | 4.4 | 4.4 | 4.4 | 4.5 | 4.5 | 4.5 | 4.6 | 4.6 | 4.6 | 4.6 | 4.7 | 4.7 | 4.7 | 4.7 | 4.8 | 4.8 | 4.8 | 4.9 | 4.9 | 4.9 | 4.9 | 5 | 5 | 5 | 5.1 | 5.1 | 5.1 | 5.1 | 5.2 | 5.2 | 5.2 | 5.3 | 5.3 | 5.3 | 5.3 | 5.4 | 5.4 | 5.4 | 5.5 | 5.5 | 5.5 | 5.5 | 5.6 | 5.6 | 5.6 | 5.7 | 5.7
Ug = 0.8, G값 = 0.25 | 4 | 4 | 4 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.4 | 4.4 | 4.4 | 4.4 | 4.4 | 4.4 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.6 | 4.6 | 4.6 | 4.6 | 4.6 | 4.6 | 4.7 | 4.7 | 4.7 | 4.7 | 4.7 | 4.7 | 4.8 | 4.8 | 4.8 | 4.8 | 4.8 | 4.8 | 4.9 | 4.9 | 4.9 | 4.9 | 4.9 | 4.9 | 5 | 5
Ug = 0.8, G값 = 0.3 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3
Ug = 0.8, G값 = 0.35 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7
Ug = 0.8, G값 = 0.4 | 4 | 4 | 4 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.8 | 3.8 | 3.8 | 3.8 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1
Ug = 0.8, G값 = 0.45 | 4 | 4 | 3.9 | 3.9 | 3.9 | 3.8 | 3.8 | 3.8 | 3.7 | 3.7 | 3.7 | 3.6 | 3.6 | 3.6 | 3.5 | 3.5 | 3.5 | 3.4 | 3.4 | 3.4 | 3.3 | 3.3 | 3.3 | 3.3 | 3.2 | 3.2 | 3.2 | 3.2 | 3.1 | 3.1 | 3.1 | 3.1 | 3 | 3 | 3 | 3 | 3 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6
Ug = 0.8, G값 = 0.5 | 4 | 4 | 3.9 | 3.9 | 3.8 | 3.8 | 3.7 | 3.7 | 3.6 | 3.6 | 3.5 | 3.5 | 3.5 | 3.4 | 3.4 | 3.3 | 3.3 | 3.2 | 3.2 | 3.2 | 3.1 | 3.1 | 3 | 3 | 3 | 2.9 | 2.9 | 2.9 | 2.8 | 2.8 | 2.8 | 2.7 | 2.7 | 2.7 | 2.7 | 2.6 | 2.6 | 2.6 | 2.6 | 2.5 | 2.5 | 2.5 | 2.5 | 2.4 | 2.4 | 2.4 | 2.4 | 2.4 | 2.3 | 2.3 | 2.3 | 2.3 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2
Ug = 0.8, G값 = 0.55 | 4 | 4 | 3.9 | 3.8 | 3.8 | 3.7 | 3.7 | 3.6 | 3.5 | 3.5 | 3.4 | 3.4 | 3.3 | 3.2 | 3.2 | 3.1 | 3.1 | 3 | 3 | 2.9 | 2.9 | 2.8 | 2.8 | 2.8 | 2.7 | 2.7 | 2.6 | 2.6 | 2.6 | 2.5 | 2.5 | 2.4 | 2.4 | 2.4 | 2.3 | 2.3 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.1 | 2.1 | 2.1 | 2.1 | 2 | 2 | 2 | 2 | 2 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.8 | 1.8 | 1.8 | 1.8
Ug = 0.8, G값 = 0.6 | 4 | 3.9 | 3.9 | 3.8 | 3.7 | 3.6 | 3.6 | 3.5 | 3.4 | 3.4 | 3.3 | 3.2 | 3.2 | 3.1 | 3 | 3 | 2.9 | 2.8 | 2.8 | 2.7 | 2.7 | 2.6 | 2.6 | 2.5 | 2.5 | 2.4 | 2.4 | 2.3 | 2.3 | 2.3 | 2.2 | 2.2 | 2.1 | 2.1 | 2.1 | 2 | 2 | 2 | 1.9 | 1.9 | 1.9 | 1.8 | 1.8 | 1.8 | 1.8 | 1.7 | 1.7 | 1.7 | 1.7 | 1.7 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5
Ug = 0.8, G값 = 0.1 | 4 | 4.1 | 4.1 | 4.2 | 4.2 | 4.3 | 4.3 | 4.4 | 4.4 | 4.5 | 4.6 | 4.6 | 4.7 | 4.7 | 4.8 | 4.8 | 4.9 | 4.9 | 5 | 5 | 5.1 | 5.1 | 5.2 | 5.3 | 5.3 | 5.4 | 5.4 | 5.5 | 5.5 | 5.6 | 5.6 | 5.7 | 5.7 | 5.8 | 5.8 | 5.9 | 5.9 | 6 | 6.1 | 6.1 | 6.2 | 6.2 | 6.3 | 6.3 | 6.4 | 6.4 | 6.5 | 6.5 | 6.6 | 6.6 | 6.7 | 6.7 | 6.8 | 6.9 | 6.9 | 7 | 7 | 7.1 | 7.1 | 7.2
g-값 : 0.20
g-값 : 0.25
g-값 : 0.30
g-값 : 0.35
g-값 : 0.40
g-값 : 0.45
g-값 : 0.50
1.8L
Chart: S. Window area (m2)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59
Ug = 0.8, G값 = 0.1 | 3.3 | 3.3 | 3.4 | 3.4 | 3.4 | 3.4 | 3.5 | 3.5 | 3.5 | 3.6 | 3.6 | 3.6 | 3.7 | 3.7 | 3.7 | 3.8 | 3.8 | 3.8 | 3.9 | 3.9 | 3.9 | 4 | 4 | 4 | 4.1 | 4.1 | 4.1 | 4.2 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.4 | 4.4 | 4.4 | 4.5 | 4.5 | 4.5 | 4.6 | 4.6 | 4.6 | 4.7 | 4.7 | 4.7 | 4.8 | 4.8 | 4.8 | 4.9 | 4.9 | 4.9 | 5 | 5 | 5 | 5.1 | 5.1 | 5.1 | 5.2 | 5.2 | 5.2
Ug = 0.8, G값 = 0.15 | 3.3 | 3.3 | 3.3 | 3.3 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.7 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9 | 4 | 4 | 4 | 4 | 4 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.1 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.2 | 4.3 | 4.3 | 4.3 | 4.3
Ug = 0.8, G값 = 0.2 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.4 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
Ug = 0.8, G값 = 0.25 | 3.3 | 3.3 | 3.3 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1 | 3.1 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.9 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7 | 2.7
Ug = 0.8, G값 = 0.3 | 3.3 | 3.3 | 3.2 | 3.2 | 3.2 | 3.1 | 3.1 | 3.1 | 3 | 3 | 3 | 3 | 2.9 | 2.9 | 2.9 | 2.8 | 2.8 | 2.8 | 2.8 | 2.7 | 2.7 | 2.7 | 2.7 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.4 | 2.4 | 2.4 | 2.4 | 2.4 | 2.3 | 2.3 | 2.3 | 2.3 | 2.3 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1
Ug = 0.8, G값 = 0.35 | 3.3 | 3.2 | 3.2 | 3.1 | 3.1 | 3.1 | 3 | 3 | 2.9 | 2.9 | 2.8 | 2.8 | 2.7 | 2.7 | 2.7 | 2.6 | 2.6 | 2.5 | 2.5 | 2.5 | 2.4 | 2.4 | 2.4 | 2.3 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.1 | 2.1 | 2.1 | 2.1 | 2 | 2 | 2 | 2 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.8 | 1.8 | 1.8 | 1.8 | 1.8 | 1.7 | 1.7 | 1.7 | 1.7 | 1.7 | 1.7 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6
Ug = 0.8, G값 = 0.4 | 3.3 | 3.2 | 3.2 | 3.1 | 3 | 3 | 2.9 | 2.9 | 2.8 | 2.7 | 2.7 | 2.6 | 2.6 | 2.5 | 2.5 | 2.4 | 2.4 | 2.3 | 2.3 | 2.2 | 2.2 | 2.1 | 2.1 | 2 | 2 | 2 | 1.9 | 1.9 | 1.8 | 1.8 | 1.8 | 1.7 | 1.7 | 1.7 | 1.7 | 1.6 | 1.6 | 1.6 | 1.5 | 1.5 | 1.5 | 1.5 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2
Ug = 0.8, G값 = 0.45 | 3.3 | 3.2 | 3.1 | 3.1 | 3 | 2.9 | 2.8 | 2.7 | 2.7 | 2.6 | 2.5 | 2.5 | 2.4 | 2.3 | 2.3 | 2.2 | 2.1 | 2.1 | 2 | 2 | 1.9 | 1.9 | 1.8 | 1.8 | 1.7 | 1.7 | 1.6 | 1.6 | 1.6 | 1.5 | 1.5 | 1.4 | 1.4 | 1.4 | 1.3 | 1.3 | 1.3 | 1.3 | 1.2 | 1.2 | 1.2 | 1.2 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
Ug = 0.8, G값 = 0.5 | 3.2 | 3.2 | 3.1 | 3 | 2.9 | 2.8 | 2.7 | 2.6 | 2.6 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2.1 | 2 | 1.9 | 1.9 | 1.8 | 1.7 | 1.7 | 1.6 | 1.6 | 1.5 | 1.5 | 1.4 | 1.4 | 1.3 | 1.3 | 1.3 | 1.2 | 1.2 | 1.2 | 1.1 | 1.1 | 1.1 | 1 | 1 | 1 | 1 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.6
Ug = 0.8, G값 = 0.55 | 3.3 | 3.2 | 3.1 | 3 | 2.8 | 2.7 | 2.6 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2.1 | 2 | 1.9 | 1.8 | 1.7 | 1.7 | 1.6 | 1.5 | 1.5 | 1.4 | 1.4 | 1.3 | 1.3 | 1.2 | 1.2 | 1.1 | 1.1 | 1 | 1 | 1 | 0.9 | 0.9 | 0.9 | 0.9 | 0.8 | 0.8 | 0.8 | 0.8 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
Ug = 0.8, G값 = 0.6 | 3.3 | 3.2 | 3 | 2.9 | 2.8 | 2.7 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2 | 1.9 | 1.8 | 1.7 | 1.6 | 1.6 | 1.5 | 1.4 | 1.3 | 1.3 | 1.2 | 1.2 | 1.1 | 1.1 | 1 | 1 | 0.9 | 0.9 | 0.9 | 0.8 | 0.8 | 0.8 | 0.7 | 0.7 | 0.7 | 0.7 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
g-값 : 0.20
g-값 : 0.25
g-값 : 0.30
g-값 : 0.35
g-값 : 0.40
g-값 : 0.45
g-값 : 0.50
2.5L
- Middle of EU
- Seoul

## Slide 28
Adjust g-value according to energy consumption pattern
  Residential facilities receive a lot of solar energy to reduce heating energy, and non-residential facilities block solar energy to reduce cooling load.
Localization of passive house - SHGC (g-value)
Residential buildings
Energy Consumption
heating
cooling
Low Internal Heat Gain
Large Internal Heat Gain
Non-Residential buildings
Energy Consumption
heating
cooling

## Slide 29
Localization of passive house - Shading
Shading

## Slide 30
Necessity of Shade
  Since the temperature and humidity are higher than in Germany, it is necessary to reduce the cooling load by actively blocking solar radiation.
Localization of passive house - Shading
Chart: temperature (℃)
독일표준 | 0.9 | 2 | 8.4 | 16.2 | 16.7 | 18.7 | 19.6 | 14.7 | 11 | 5.9 | 1.7
서울 | -2 | 0.8 | 13.1 | 18.2 | 22.7 | 25.3 | 25.5 | 21.6 | 14.6 | 7.4 | 0.7
- South solar radiation
- Outdoor temperature
More Humidity
More Hot
Seoul
Germany

## Slide 31
Short wave
long wave
Localization of passive house - Shading
The need for an external awning
  Short-wave solar energy that enters through the transparent building material turns into a long-wave and heats the inside.

## Slide 32
Various type of shading
  There are sun protection devices of various materials.
  A shading device considering the design of the building should be planned from the beginning of the design.
Localization of passive house - Shading

## Slide 33
Localization of passive house - Shading
Fixed awning plan
  Draw a line with the latitude of the area based on the center of the glass.
  Extrude the structure close to the line.
May
June
July
August
September
October
November
December
Shadow at 2pm on the 15th of each month
latitude
center of the glass

## Slide 34
Localization of passive house – Envelope U-value
Envelope U-value

## Slide 35
Localization of passive house – Envelope U-value
- Heat Degree Hours in South Korea
- current law and Organized by region
Exterior wall insulation standards based on climate data
  Insulation performance analysis to prevent condensation mold in the corner of the exterior wall

## Slide 36
Localization of passive house – Envelope U-value
Window Performance by Climate
  The temperature difference between the inner wall and the window surface is 3K or less
  Conditions under which cold drafts do not occur around windows
Conditions that do not generate cold drafts based on the coldest 12-hour winter temperature interval Uw = 4.2K / [1.1(m2K/W) X (22℃ - Ext. Temp.)]
Height 0.1m
Height 1.1m
Radiation temperature difference < 3K
Temperature difference must be smaller than 2K – cold feet
The coldest 12-hour
average temperature
(W/㎡K)

## Slide 37
Localization of passive house – Thermal Storage
Thermal Storage

## Slide 38
Localization of passive house – Thermal Storage
Large temperature differences between day and night
  Due to the large temperature difference between day and night, it is necessary to plan for facility response capability and comfort level management.
+ 15 °C
-270.45 °C

## Slide 39
Localization of passive house – Thermal Storage
Effect of heat storage performance
  By using the thermal storage performance, it is possible to prevent the indoor temperature from changing rapidly when the outside temperature changes greatly.

## Slide 40
Localization of passive house – lifestyle
Lifestyle

## Slide 41
Localization of passive house – lifestyle
Different lifestyle
  The floor heating method used in Korea for more than 1000 years is being applied to residential facilities in a modified form in modern architecture.

## Slide 42
Localization of passive house – lifestyle
Criteria suitable for local residential culture
  In early days of Korean passivehouse, heat is stored in mortal with high-temperature boiler. And it got worse when it release its heat during morning, the time when it starts to obtain solar radiation. It cause an overheating and people tend to open the window because of it.
Building performance (Calculated value), kWh/㎡a
Heating
Energy
demand
PHI Standard
Korea
210 kWh/㎡a
50 kWh/㎡a
15 kWh/㎡a

## Slide 43
Localization of passive house – lifestyle
Passive House standard in PHIKO
 |  | German | Korea
U-value | Ex. Wall | 0.15 W/㎡·K | 0.15 ~ 0.18 W/㎡·K
 | roof | 0.15 W/㎡·K | 0.12 ~ 0.15 W/㎡·K
 | U-glass | 0.8 W/㎡·K | 0.9 ~ 1.4 W/㎡·K
 | U-frame | 0.8 W/㎡·K | 0.8 ~ 1.4 W/㎡·K
 | U-window | 0.85 W/㎡·K | 0.9 ~ 1.5 W/㎡·K
 | door | 0.8 W/㎡·K | 1.2 W/㎡·K
g-value | glass g-value (SHGC) | 0.5 | 0.4
Heat Exchanger | Efficiency | 75% | 75%
 | Power Consumption | 0.45 W/㎥h | 0.50 W/㎥h
Performance | Air tightness | 0.6 /h @ 50Pa | 1.0 /h @ 50Pa
 | Heating Demand | 15 kWh/㎡a | 50 kWh/㎡a
 | primary energy consumtion | 120 kWh/㎡a | 150 kWh/㎡a

## Slide 44
Localization of passive house

## Slide 45
Localization of passive house
Tashkent City Park

## Slide 46
Localization of passive house
Tashkent City Park – climate data

## Slide 47
Heating demand Seoul & Tashkent City Park
  The same building was compared by applying the climates of Seoul and Tashkent.
Seoul
Tashkent City Park
27.06
kWh/㎡a
21.59
kWh/㎡a
Localization of passive house

## Slide 48
Zero Energy Building - EDC

## Slide 49
Zero Energy Building - EDC
88.92kW
57.4kW
45.7 kW
- Detached house energy self-sufficiency rate 109%
- Public Relations Hall Housing Energy Self-Reliance Rate171%
solar power panel

## Slide 50
Zero Energy Building - EDC
Geothermal source heat pump system & Water source heat pump system

## Slide 51
Zero Energy Building - EDC
Geothermal source heat pump system & Water source heat pump system

## Slide 52
Zero Energy Building - EDC
Energy sharing platform development and business model development