## Slide 1: BIM & Smart Construction Technologies for Tracking the Construction Process and Problem Identification at the Early Stages of Construction
Lee, Jin Gang
Sunmoon University

## Slide 2
이진강 (Lee, Jin Gang)
jinganglee@sunmoon.ac.kr
Education
  Bachelor, Seoul National University (2007 – 2011) Dept. of Architecture and Architecture Engineering
  Master of Science, Seoul National University (2011 – 2013) Construction Engineering and Management Laboratory Thesis: BIM based Cost-Schedule Integration using IFC for Building Construction
  Doctor of Philosophy, Seoul National University (2013 – 2019) Construction Engineering and Management Laboratory Thesis:Conceptual Estimation of Construction Cost by Neural Network Ensemble Learning incorporating Factor Analysis
Experiences
  Assistant Professor, Sunmoon University, Division of Architecture (2021 ~ present)
  Postdoctoral Fellow, The Hong Kong Polytechnic University, Dept. of Building and Real Estate (2019 ~ 2020)
  Researcher, Seoul National University Institute of Construction and Environmental Engineering (2019)
Research Interest & Teaching Area
  BIM Applications for Design Collaboration and Construction Management
  Smart Construction Technologies: Virtual Reality, Augmented Reality, Machine Learning, Computer Vision
  Construction Management: Schedule, Cost, Safety, Quality
Lecturer

## Slide 3
Background
Building Information Modeling (BIM)
  Definition
  Problem Identification at the Early Stages of Construction
Smart Construction
  Definition
  Technologies for Tracking the Construction Process
Contents

## Slide 4
Construction Productivity
  Empire State Building (New York, 1930)
  Lotte World Tower (Seoul, 2016)
Background
vs

## Slide 5
Productivity of Construction Industry
  The construction industry is known as a typical high cost and low productivity industry.
Background
Reference: Mckensey (2017), Reinventing Construction

## Slide 6
Productivity of Construction Industry
  The construction industry is known as a typical high cost and low productivity industry.
  In the case of South Korea, it is growing every year, but it is only half of the global average.
Background
Reference: Mckensey (2017), Reinventing Construction

## Slide 7
Digitalization of Construction Industry
  Contrary to the 4th industrial revolution, the level of digitization in the construction industry is low.
  Construction industry requires digital transformation.
Background
Reference: Mckensey (2016), Imagining Constructions Digital Future

## Slide 8
Project Management
  Plan / Execute / Manage elements of resources in accordance with project goals to produce the final product of a construction project.
Project Information Management
  Project information management is to efficiently collect, share, and process information necessary for project planning and management so that it can be used effectively and managed so that it can be used as data for future plans, etc.
Building Information Modeling
Image Source: https://www.saviom.com/index.php
Resources: Equipment, Labor, Material
Goals: Time, Cost, Quality, Safety
Information: Drawing, Schedule, Cost, Law

## Slide 9
Definition
  BIM is the creation and management of information necessary for various decision-making of a construction project in a computer-interpretable form (digital) based on the object of the 3D model (object-oriented).
Building Information Modeling
window
column
door
Project Information DB
Object-oriented Modeling
cost
schedule
law
properties
Cost
Schedule
Drawing
Integrated Management
Image Source: Succar, B. (2009); doi:10.1016/j.autcon.2008.10.003

## Slide 10
Design Coordination / Collaboration
  A collaborative process between various specialties such as architecture, structure, MEP, etc..
  Design collaboration is the process of integrating design proposals from individual specialties.
Building Information Modeling

## Slide 11
Design Coordination / Collaboration
  There are hundreds or thousands of issues to be resolved in the design collaboration process, which consumes considerable time.
Building Information Modeling
24 hours
per week
40-50% of total work hours
Some meetings often take 3 hours

## Slide 12
3D Visualization
  2D vs 3D
Building Information Modeling

## Slide 13
3D Visualization
  2D: Separated, Manual → Error prone, Time-consuming
  3D: Integrated, Digital → Effective Communication
Building Information Modeling
vs

## Slide 14
3D Visualization
  Model-based Design Coordination Process
Building Information Modeling
Model Creation
Model Management
Communication
Owner
Architect
Contractor
Subcontractor
Engineer
Construction Manager
MEP
Facility Manager
Create and submit model (BIM authoring tools)
Analyze the model and identify issues. (BIM analysis tools)
Create coordination documents
Add issue related information on model or coordiantion document
Check information of issues (in both model and document)
Create coordination documents
Add issue related information on model or coordiantion document

## Slide 15
Clash Check
  Clash is an unintentional overlap between different objects or too close together so that construction is impossible in that state.
Building Information Modeling
Image Source: https://bimtrack.co/blog/blog-posts/clash-detection-vs-quality-control-the-differences

## Slide 16
Clash Check
  Hard Clash
  Two or more objects exist in the same space.
Building Information Modeling

## Slide 17
Clash Check
  Soft Clash
  Two or more objects do not directly overlap, but require the same space.
  Insufficient space between objects causes difficulties in construction or use of buildings on site..
Building Information Modeling

## Slide 18
Clash Check
  4D / Workflow Clash
  Depending on the progress or on-site situation, collisions of objects and duplication of required space occur.
  The movement of temporary works and materials during construction is the main cause of workflow clash.
Building Information Modeling
Image Source: Swallow, Mark Richard, and Sam Zulu. "Benefits and Barriers to the Adoption of 4D Modelling for Site Health and Safety Management." Frontiers in Built Environment 4 (2018): 86.

## Slide 19
4D Simulation
  4D = 3D + Time (referred to as 4D by adding the concept of time to the 3D model).
  Model the building shape or site situation during construction, which changes every moment.
Building Information Modeling
Revit Architecture – Modeling
Navisworks – 4D Sequencing

## Slide 20
4D Simulation
  Import the activity created in the project management software (Primavera, MS Project)
  Link BIM objects related to each activity.
Building Information Modeling
<3D Model (Revit)>
<Project Schedule (e.g., MS Project)>
Navisworks Exporter
Import a schedule file
Create a schedule in Navisworks

## Slide 21
4D Simulation
  Checking the actual construction plan in three-dimensional
  Analyze the feasibility of the process plan or the retrieval plan in the virtual site.
Building Information Modeling
Navisworks – 4D Sequencing
Image Source: Autodesk University

## Slide 22
4D Simulation
  Help on-site management and safety management by enabling many project participants in the field to consistently understand the situation at the site.
  The work space according to the construction sequence is checked in 3D, and information about the process by specialized company such as interior/exterior, equipment, etc. is reviewed with the person concerned to facilitate consultation.
Building Information Modeling
Image Source: Autodesk University

## Slide 23
4D Simulation
  Review whether it is possible to bring in or store heavy and long equipments or materials at the site.
  Various factors can be taken into account, such as materials, equipment, and surrounding traffic conditions.
Building Information Modeling
Modeling the swing of a crane or the lifting of a steel frame, so that the flow of construction can be reviewed from various angles
Revit Architecture/Sketchup/Google Earth – Site Coordination

## Slide 24
Pre-construction Meeting
  (1) Submit individual models of architecture, structure, machinery, equipment, etc.
  Individual companies are also required to have 3D BIM modeling skills to participate BIM project.
  (2) Integral analysis of 3D models of individual specialist companies.
  Using software such as Navisworks.
  (3) Communicate with the discovered issues and adjust the design (model).
  It is effectively used to find problems between members of different types of construction by specialized companies throughout the design stage, pre-construction stage, and construction stage.
Building Information Modeling

## Slide 25
Pre-construction Meeting
  Iterative collaboration process
Building Information Modeling
Image Source: (1) http://bimstar.co.in/clash-detection-clash-reports/ (2) http://www.revitmodelingindia.com/services/bim-clash-detection-services/

## Slide 26
Pre-construction Meeting
  Preliminary identification of on-site issues in the design stage and pre-construction stage → Reduction of rework → Shorten construction period, save construction cost
Building Information Modeling
BIM Effort
Image Source: MacLeamy curve (2004)

## Slide 27
BIM Applications
  One of the biggest benefits contractors can get from using BIM
  Great improvement in resolving clash, understanding construction details, identifying drawing errors.
Building Information Modeling
Image Source: B. Becerik-Gerber and S. Rice, The perceived value of building information modeling in the US building industry, J. of Information Technology in Construction, 15, 185-201, (2010)

## Slide 28
BIM Applications
  One hundred percent of MEP contractors and 90 percent of general contractors and structural engineers surveyed report participating in such integrated workflows — with tangible benefits to show for it.
Building Information Modeling
Image Source: https://projectdelivery.autodesk.com/blog/aec-industry-trends-bim-dodge-analytics/

## Slide 29
BIM Applications
  Starting with the US and Europe, national institutions and companies are actively promoting BIM introduction policies including guidelines and information standards.
Building Information Modeling
Image Source: https://www.geospatialworld.net/article/bim-adoption-around-the-world-how-good-are-we/

## Slide 30
BIM Applications
  In South Korea, the Ministry of Land, Infrastructure and Transport continues to promote BIM activation policies in all fields of construction, civil engineering, and engineering and to prepare BIM mandatory plan and order for pilot project
Building Information Modeling
Image Source: the Korea Institute of Civil Engineering and Building Technology
BIM도입 활성화를 위한 국가정책
장단기 계획 (2009) : 10 년간 추진계획
세움터 고도화 기본계획 (2009) :
인허가 지능형 서비스에 BIM 도입
제 6 차 건설기술진흥기본계획 (2017) :
스마트 건설구현위한 BIM 핵심기술 적용
제 5 차 건설사업정보화진흥계획 (2017) :
인프라 BIM 활성화 및 플랫폼 개발
국토교통부 (2015) : 2020년까지 사회기반시설 (SOC) 공사 20% BIM 적용
국토교통부 (2017) : 2020년까지 500억 이상 공사 대상 BIM 발주 의무화
2016 년 : 시설사업 BIM 적용지침서 v 1.31 발표
2016 년부터 시설사업 전체 대상 BIM 발주 (50건, 2조 규모)
2017 년부터 입찰 시 BIM 도면 및 보고서 의무화
2011 년 : BIM 가이드라인 발표
2017 년 : Civil – BIM 도입 착수
2009 년 : 공동 주택 최초 BIM 현상 설계 도입
양주 회천지구
파주 운정지구
2013 년 : BIM 마스터플랜 발표
2017 년부터 전사적 체계 구축
시법사업 수행
낙동강 살리기 4개공구
영주댐, 보현산댐
대산임해산업지역 공업용수도
2014 년 : BIM 마스터플랜 발표
2015 년 : BIM 가이드라인 v 1.0
시법사업 수행
부산외곽순환 고속도로
대구순환 고속도로
함양울산간 고솔도로

## Slide 31
BIM Applications
  2010: 43% don't know BIM
  2020: 73% use BIM
Building Information Modeling
Image Source: https://www.thenbs.com/knowledge/national-bim-report-2020

## Slide 32
Future of BIM
  4th Industrial Revolution
Building Information Modeling
Image Source: https://www.thenbs.com/knowledge/national-bim-report-2020

## Slide 33
4th Industrial Revolution
  The next-generation industrial revolution brought about by the convergence of information and communication technology (ICT).
  New technological innovations in areas such as big data analytics, artificial intelligence, robotics, Internet of Things, unmanned vehicles (drones, unmanned vehicles), 3D printing, and AR/VR technologies.
Smart Construction
Image Source: http://news.unist.ac.kr/kor/column_202/

## Slide 34
Smart Construction
  Various technologies to innovate productivity based on information sharing and connectivity of all participants in all stages of construction work, such as planning, design, construction, maintenance, and demolition, using the 4th industrial revolution element technology
Smart Construction
Image Source: Ministry of Land, Infrastructure and Transport

## Slide 35
Smart Construction
  Experience-dependent industry → Paradigm shift to knowledge and high-tech industry
  Overcoming the limitations of manpower → Improving productivity and safety
Smart Construction
Image Source: Ministry of Land, Infrastructure and Transport

## Slide 36
Smart Construction
  Experience-dependent industry → Paradigm shift to knowledge and high-tech industry
  Overcoming the limitations of manpower → Improving productivity and safety
Smart Construction
Source: Ministry of Land, Infrastructure and Transport
As-is | To-be
Data-oriented Decision Making | 
Separated information | Information sharing and distribution
Experience-dependent | Optimization through data analysis
Repetition of trial and error | Prediction through simulation
Technology Convergence | 
Separated individual | Activation of technology application
Segmentation by stages | Integration of all stages of construction
Manual and repetitive work | Communication and collaboration
Consumer-oriented technology | 
Skilled labor | Automate workforce
2D | 3D + α
Supplier-centric | Consumer participation

## Slide 37
Smart Construction
  Application technologies: big data analytics, artificial intelligence, robotics, Internet of Things, unmanned vehicles (drones, unmanned vehicles), 3D printing, and AR/VR technologies.
Smart Construction
Category | Technologies for Smart Construction
Platform | BIM, Cloud
Data collection | IoT, Sensor, Drone (UAV), Robotics
Data analysis | Big Data Analytics, Artificial Intelligence
Automatic Manufacture | Modular construction, 3D Printing
Applications | Virtual Reality, Augmented Reality

## Slide 38
Smart Construction
  Design stages
Smart Construction
Source: Ministry of Land, Infrastructure and Transport

## Slide 39
Smart Construction
  Construction stages
Smart Construction
Source: Ministry of Land, Infrastructure and Transport
Finishing

## Slide 40
Smart Construction
  Operation and management stages
Smart Construction
Source: Ministry of Land, Infrastructure and Transport

## Slide 41
BIM & Smart Construction
  Reverse engineering : Obtain design / engineering information of the building through 3D scanning or sensor and use it for project management (construction, maintenance).
BIM & Smart Construction
Source: Utilization of 3D scanner and BIM for uprising 4th industrial revolution

## Slide 42
BIM & Smart Construction
  Virtual Reality / Augmented Reality: A number of studies have been conducted examining the utility of immersive VR/AR for promoting architectural design collaboration, project site management, worker safety education in a more immersive environment by implementing BIM project information in a virtual space.
BIM & Smart Construction
Image Source: JBKnowledge (2015), BIManywhere (2015)

## Slide 43
BIM & Smart Construction
  More than 20 years have passed since BIM was applied in the construction field.
  As successful cases of BIM project are shared, the need to apply BIM and the will to adopt it arises.
  At the same time, skepticism about BIM arose as several failure cases were accumulated.
  It is judged to be a stage of re-lighting in Gartner's Hype-cycle.
BIM & Smart Construction
Image Source: Hype-cycle (Gartner)
Integrated project management
Productivity improvement
Project success
Initial investment
Added work process
Apply BIM for showing
Digital project management
Industry competitiveness
Platform for smart construction
BIM do all
BIM skepticism
BIM again ?

## Slide 44
Summary
  Problem Identification at the Early Stages of Construction
  Technologies for Tracking the Construction Process
BIM & Smart Construction
Safety
Time
Quality
Cost
BIM & Smart Construction
Low Productivity
Low Digitalization
Post-Corona
Labor Intensive